## Slide 1
Mountainboard - Lesson 2
Basic Functionality
School’s Name
Teacher’s Name
Date

## Slide 2: What is SolidWorks?
SolidWorks is design automation software.
In SolidWorks, you sketch ideas and experiment with different designs to create 3D models.
SolidWorks is used by students, designers, engineers, and other professionals to produce simple and complex parts, assemblies, and drawings.

## Slide 3: The SolidWorks Model
The SolidWorks model is made up of:
  Parts
  Assemblies
  Drawings

## Slide 4: The SolidWorks Model
Part
Part
Assembly
Drawing
Drawing

## Slide 5: Features
Features are the building blocks of the part.
Features are the shapes and operations that construct the part.

## Slide 6: Examples of Shape Features
Base Feature
  First feature in part.
  Created from a 2D sketch.
  Forms the work piece to which other features are added.

## Slide 7: Examples of Shape Features
Boss feature
  Adds material to part.
  Created from 2D sketch.

## Slide 8: Examples of Shape Features
Cut feature
  Removes material from part.
  Created from 2D sketch.

## Slide 9: Examples of Shape Features
Hole feature
  Removes material.
  Works like more intelligent cut feature.
  Corresponds to process such as counter-sink, thread, counter-bore.

## Slide 10: Examples of Shape Features
Fillet feature
  Used to round off sharp edges.
  Can remove or add material.
    Outside edge (convex fillet) removes material.
    Inside edge (concave fillet) adds material.

## Slide 11: Examples of Shape Features
Chamfer feature
  Similar to a fillet.
  Bevels an edge rather than rounding it.
  Can remove or add material.

## Slide 12: Sketched Features & Operation Features
Sketched Features
  Shape features have sketches.
  Sketched features are built from 2D profiles.
Operation Features
  Operation features do not have sketches.
  Applied directly to the work piece by selecting edges or faces.

## Slide 13: To Create an Extruded Base Feature:
Sketch the 2D profile
Select a sketch plane.
Sketch a 2D profile.
Extrude the sketch perpendicular to sketch plane.
Select the sketch plane
Extrude the sketch
Resulting base feature

## Slide 14: To Create a Revolved Base Feature:
Select a sketch plane.
Sketch a 2D profile.
Sketch a centerline (optional).
Revolve the sketch around a sketch line or centerline.
Centerline (optional)

## Slide 15: Terminology: Document Window
Divided into two panels:
  Left panel contains the FeatureManager® design tree.
    Lists the structure of the part, assembly or drawing.
  Right panel contains the Graphics Area.
    Location to display, create, and modify a part, assembly or drawing.
FeatureManager design tree
Graphics Area

## Slide 16: Terminology: User Interface
Toolbar
Menu Bar
Task pane
Status bar
Command Manager
Drawing document window
Part document window

## Slide 17: Terminology: PropertyManager
Property Manager
Confirmation corner
Preview
Handle

## Slide 18: Terminology: Basic Geometry
Axis - An implied centerline that runs through every cylindrical feature.
Plane - A flat 2D surface.
Origin - The point where the three default reference planes intersect. The coordinates of the origin are: (x = 0, y = 0, z = 0).
Axis
Plane
Origin

## Slide 19: Terminology: Basic Geometry
Face The surface or “skin” of a part. Faces can be flat or curved.
Edge The boundary of a face. Edges can be straight or curved.
Vertex The corner where edges meet.
Vertex
Edge
Edge
Faces

## Slide 20: Features and Commands
Base feature
The Base feature is the first feature that is created.
The Base feature is the foundation of the part.
The Base feature geometry for the box is an extrusion.
The extrusion is named Extrude1.

## Slide 21: Features and Commands
Features used to build the box are:
Extruded Base feature
Fillet feature
Shell feature
Extruded Cut feature
1.Base Feature
2.Fillet Feature
3.Shell Feature
4.Cut Feature

## Slide 22: Features and Commands
To create the extruded base feature for the box:
Sketch a rectangular profile on a 2D plane.
Extrude the sketch.
By default extrusions are perpendicular to the sketch plane.

## Slide 23: Features and Commands
Fillet feature
The fillet feature rounds the edges or faces of a part.
Select the edges to be rounded. Selecting a face rounds all the edges of that face.
Specify the fillet radius.
Fillet

## Slide 24: Features and Commands
Shell feature
The shell feature removes material from the selected face.
Using the shell feature creates a hollow box from a solid box.
Specify the wall thickness for the shell feature.
Wall Thickness

## Slide 25: Features and Commands
To create the extruded cut feature for the box:
Sketch the 2D circular profile.
Extrude the 2D Sketch profile perpendicular to the sketch plane.
Enter Through All for the end condition.
The cut penetrates through the entire part.

## Slide 26: Dimensions and Geometric Relationships
Specify dimensions and geometric relationships between features and sketches.
Dimensions change the size and shape of the part.
Mathematical relationships between dimensions can be controlled by equations.
Geometric relationships are the rules that control the behavior of sketch geometry.
Geometric relationships help capture design intent.

## Slide 27: Dimensions
Dimensions
  Base depth = 50mm
  Boss depth = 25mm
Mathematical relationship
  Boss depth = Base depth  2

## Slide 28: Geometric Relationships
Tangent
Parallel
Horizontal
Vertical
Intersection
Concentric
Perpendicular

## Slide 29: To Start SolidWorks
Click the Start button on Windows task bar.
  Click All Programs.
    Click the SolidWorks folder.
      Click the SolidWorks application.

## Slide 30: The SolidWorks Window

## Slide 31: Creating New Files Using Templates
Click New on the Standard toolbar.
Select a document template:
  Part
  Assembly
  Drawing
Tutorial Tab

## Slide 32: Document Templates
Document Templates control the units, grid, text, and other settings for the model.
The Tutorial document templates are required to complete the exercises in the Online Tutorials.
The templates are located in the Tutorial tab on the New SolidWorks Document dialog box.
Document properties are saved in templates.

## Slide 33: Document Properties
Accessed through the Tools, Options menu.
Control settings like:
  Units: English (inches) or Metric (millimeters)
  Grid/Snap Settings
  Colors, Material Properties and Image Quality

## Slide 34: System Options
Accessed through the Tools, Options menu.
Allow you to customize your work environment.
System options control:
  File locations
  Performance
  Spin box increments

## Slide 35: Multiple Views of a Document
Click the view pop-up menu.
Select an icon. The viewport icons include:
  Single View
  Two View (horizontal and vertical)
  Four View

## Slide 36: Creating a 2D Sketch
Click Sketch on the Sketch toolbar.
Select the Front plane as a sketch plane.
Click Rectangle on the Sketch Tools toolbar.
Move the pointer to the Sketch Origin.

## Slide 37: Creating a 2D Sketch
Click the left mouse button.
Drag the pointer up and to the right.
Click the left mouse button again.

## Slide 38: Adding Dimensions
Dimensions specify the size of the model.
To create a dimension:
Click Smart Dimension on the Dimensions/Relations toolbar.
Click the 2D geometry.
Click the text location.
Enter the dimension value.
2D geometry
Text location

## Slide 39: The Mountainboard

## Slide 40: Design Process
Project goals.
  Design Intent
    How does the model respond to change
    Anticipated changes in the design
  Analysis
    Estimation of the lifecycle of the product
    How will we insure that the parts are strong enough
  Output
    Engineering reports
    Presentations
    Marketing material

## Slide 41: Key parts
The Binding
  Right and Left versions
  Adjusts position
    Rotation
    Along Deck

## Slide 42: Key parts
The Deck
  Flexible
  Mounting for Binding and Truck
  Non-slip surface
  Support a 100 kg rider
Truck and Axle
  Adjustable suspension
  Mounting for optional braking system

## Slide 43: Key parts
Wheel Assembly
  Easy to assemble
  Tire and Tube are purchased parts
  Sealed bearings
  Mounting for optional braking system

## Slide 44: Binding Anchor

## Slide 45: Design Intent - Binding Anchor
Clamps and Positions the Binding on the Deck
Positioning
  Along centerline
  At angle to centerline
No sharp edges to injure a rider

## Slide 46: Determining the Weight
Weight = Volume X Density
Volume can be calculated from the geometry of the model
Density can be obtained from handbooks, data sheets or online

## Slide 47: Mass Properties
The Mass Properties tool can calculate:
Volume
Mass
Surface Area
Center of Mass
Moments of Inertia

## Slide 48: First Angle Projection
Like projecting the model on a screen behind the model.
Used in Europe.
Right
Front
Top

## Slide 49: Third Angle Projection
Like looking at the part inside of a glass box.
Used in the United States.
Right
Front
Top

## Slide 50: Section View
Cuts the model to reveal detail.