## Slide 1: Mountianboard - Lesson 3 Basic Parts – The Binding
School’s Name
Teacher’s Name
Date

## Slide 2: Features and Commands
Base Feature
The first feature that is created.
The foundation of the part.
The base feature geometry for the box is an extrusion.
The extrusion is named Extrude1.
Tip: Keep the base feature simple.

## Slide 3: To Create an Extruded Base Feature:
Sketch the 2D profile
Select a sketch plane.
Sketch a 2D profile.
Extrude the sketch perpendicular to sketch plane.
Select the sketch plane
Extrude the sketch
Resulting base feature

## Slide 4: Features Used to Build Tutor1
1.Base Extrude
2.Boss Extrude
3.Cut Extrude
4.Fillets
5.Shell

## Slide 5: Features Used to Build Tutor1
Extruded Boss Feature
  Adds material to the part.
  Requires a sketch.
Extruded Cut Feature
  Removes material from the part.
  Requires a sketch.
Fillet Feature
  Rounds the edges or faces of a part to a specified radius.

## Slide 6: Features Used to Build Tutor1
Shell Feature
  Removes material from the selected face.
  Creates a hollow block from a solid block.
  Very useful for thin-walled, plastic parts.
  You are required to specify a wall thickness when using the shell feature.

## Slide 7: View Control
Magnify or reduce the view of a model in the graphics area.
Zoom to Fit – displays the part so that it fills the current window.
Zoom to Area – zooms in on a portion of the view that you select by dragging a bounding box.
Zoom In/Out – drag the pointer upward to zoom in. Drag the pointer downward to zoom out.
Zoom to Selection – the view zooms so that the selected object fills the window.

## Slide 8: Display Modes
Illustrate the part in various display modes.
Wireframe
Hidden lines Visible
Hidden Lines
Removed
Shaded With
Edges
Shaded

## Slide 9: Standard Views
Isometric
View
Top View
Back View
Left View
Front View
Right View
Bottom View

## Slide 10: View Orientation
Front
Right
Bottom
Isometric
Top
Left
Back
Normal To (selected plane or planar face)
Changes the view display to correspond to one of the standard view orientations.

## Slide 11: View Orientation

## Slide 12: View Orientation
The views most commonly used to describe a part are:
  Top View
  Front View
  Right View
  Isometric View

## Slide 13: Default Planes
Default Planes
  Front, Top, and Right
Correspond to the standard principle drawing views:
  Front = Front or Back view
  Top = Top or Bottom view
  Right = Right or Left view

## Slide 14: Isometric View
Displays the part with height, width, and depth equally foreshortened.
  Pictorial rather than orthographic.
  Shows all three dimensions – height, width, and depth.
  Easier to visualize than orthographic views.

## Slide 15: Section View
Displays the internal structure of a model.
Requires a section cutting plane.
Section Plane

## Slide 16: The Status of a Sketch
Under defined
  Additional dimensions or relations are required.
  Under defined sketch entities are blue (by default).
Fully defined
  No additional dimensions or relationships are required.
  Fully defined sketch entities are black (by default).
Over defined
  Contains conflicting dimensions or relations, or both.
  Over defined sketch entities are red (by default).

## Slide 17: Geometric Relations
Geometric relations are the rules that control the behavior of sketch geometry.
Geometric relations help capture design intent.
Example: The sketched circle is concentric with the circular edge of the extruded boss feature.
In a concentric relation, selected entities have the same center point.

## Slide 18: Geometric Relations
The SolidWorks default name for circular geometry is an Arc#.
SolidWorks treats circles as 360° arcs.

## Slide 19: Degrees of Freedom: There are Six
They describe how an object is free to move.
Translation (movement) along X, Y, and Z axes.
Rotation around X, Y, and Z axes.

## Slide 20: Mate Relationships
Mates relationships align and fit together components in an assembly.
The Tutor assembly requires three mates to fully define it. The three mates are:
Coincident between the top back edge of Tutor1 and the edge of the lip on Tutor2.
Tutor1
Tutor2
Edges

## Slide 21: Mate Relationships
Second Mate: Coincident mate between the right face of Tutor1 and the right face of Tutor2.
Third Mate: Coincident mate between the top face of Tutor1 and the top face of Tutor2.

## Slide 22: Mates and Degrees of Freedom
The first mate removes all but two degrees of freedom.
The remaining degrees of freedom are:
  Movement along the edge.
  Rotation around the edge.

## Slide 23: Mates and Degrees of Freedom
The second mate removes one more degree of freedom.
The remaining degree of freedom is:
  Rotation around the edge.

## Slide 24: Mates and Degrees of Freedom
The third mate removes last degree of freedom.
No remaining degrees of freedom.
The assembly is fully defined.

## Slide 25: Binding Base Plate

## Slide 26: Design Intent
There will be two versions: left foot and right foot
Binding will be held in place by the Binding Anchor
The front and back (toe and heel ends) will curve upward
Side tabs will help to hold the foot centered
Side tabs will have slots to attach the flexible straps that go over the foot

## Slide 27: Manufacturing
Part will be cut from flat piece and bent to final shape
Use sheet metal functions to create a flat pattern

## Slide 28: Flip Side To Cut
An Extruded Cut can remove either the material inside or outside the sketch
Sketch