## Slide 1: Mountainboard - Lesson 6 Multibody Parts – The Axle and Truck
School’s Name
Teacher’s Name
Date

## Slide 2: Multibody Parts
Multibody parts occur when there is more than one continuous solid in the same part file.

## Slide 3: Creating a Multibody
Multibodies can be created with the following commands:
  Extruded bosses and cuts
  Revolved bosses and cuts
  Swept bosses and cuts
  Lofted bosses and cuts
  Thickened cuts
  Cavities

## Slide 4: Combine Command
The Combine command creates a single solid body by:
  Adding
  Subtracting
  Common

## Slide 5: Body Addition
Individual bodies add together to form a single body
Adding Bodies 1, 2 and 3
Body 2
Result
Body 3
Body 1

## Slide 6: Subtract Bodies
One body volume is removed from the other volume
Subtracting Body 1 from Body 2
Body 2
Result
Body 1

## Slide 7: Common Body
The resulting body is the volume common to initial volumes
Also known as an Intersection
Combining Bodies 1 and 2 using Common
Body 2
Result
Body 1

## Slide 8: Axle and Truck
Truck
Axle

## Slide 9: The Axle
The Axle is the connection between the wheels and the Truck.

## Slide 10: Design Intent
Connects the wheels to the Truck
Part will be machined from aluminum stock
Part will pivot about the King Pin that goes through the Truck
Mounting must be provided for optional brake system

## Slide 11: SolidWorks Simulation
SolidWorks Simulation provides a more in depth FEA package than SolidWorks SimulationXpress
The levels of SolidWorks Simulation software
  SolidWorks SimulationXpress
  SolidWorks Simulation
  SolidWorks Simulation Professional
  SolidWorks Simulation Premium

## Slide 12: Terms
Some important terms in analysis
Stress
  Tensile Stress
  Shear Stress

## Slide 13: Terms
Strain
  Elongation divided by initial length
Modulus of Elasticity
Poison’s Ratio
  Reduction in cross section
  Ratio of axial strain to cross section strain

## Slide 14: Steps in the FEA Process
Pre-processing
Solution
Post-processing

## Slide 15: Build Mathematical Model

## Slide 16: Build Finite Element Model

## Slide 17: Limitations of SolidWorks Simulation
Material is linear
  Stress is proportional to Strain
  Slope of curve is Young’s Modulus (Modulus of Elasticity)

## Slide 18: Limitations of SolidWorks Simulation
Deformations are small
  Deformation normally less than 5%
Loads are static
  Slowly applied
  Non-changing
Small Deformation
Large Deformation

## Slide 19: The Truck
The Truck holds the King Pin which is the shaft around which the Axle pivots.

## Slide 20: Design Intent
One face mounts solidly to the Deck
Bearings mounted to allow King Pin to pivot
Hex nuts will be molded into the Truck for suspension adjustment

## Slide 21: Stress Results

## Slide 22: Displacement Results

## Slide 23: Factor Of Safety