## Slide 1: Mountainboard - Lesson 9 Presenting Results
School’s Name
Teacher’s Name
Date

## Slide 2: Engineering Drawings
Drawings communicate three things about the objects they represent:
  Shape – Views communicate the shape of an object.
  Size – Dimensions communicate the size of an object.
  Other information – Notes communicate non-graphic information about manufacturing processes such as drill, ream, bore, paint, plate, grind, heat treat, remove burrs, and so forth.

## Slide 3: Sample Engineering Drawing

## Slide 4: General Drawing Rules – Views
The general characteristics of an object will determine what views are required to describe its shape.
Most objects can be described using three properly selected views.
  Sometimes you can use fewer.
  However, sometimes more are needed.

## Slide 5: Drawing Views
Why do we need three views?
  The Front and Top views of both parts are identical.
  The Right side view is necessary to show the characteristic shape.

## Slide 6: Drawing Views: When Three is not Enough
Three standard views do not fully describe the shape of the cut-out in the angled face.

## Slide 7: Drawing Views: When Three is too Many
The Right side view is unnecessary.

## Slide 8: Dimensions
There are two kinds of dimensions:
  Size dimensions – how big is the feature?
  Location dimensions – where is the feature?
Size
Dimensions
Location
Dimensions

## Slide 9: General Drawing Rules – Dimensions
For flat pieces, give the thickness dimensions in the edge view, and all other dimensions in the outline view.

## Slide 10: General Drawing Rules – Dimensions
Dimension features in the view where they can be seen true size and shape.
Use diameter dimensions for circles.
Use radial dimensions for arcs.

## Slide 11: General Drawing Rules – Dimensions
Omit unnecessary dimensions.
This
Not This

## Slide 12: Dimension Guidelines – Appearance
Place dimensions away from the profile lines.
Allow space between individual dimensions.
A gap must exist between the profile lines and the extension lines.
The size and style of leader line, text, and arrows should be consistent throughout the drawing.
Display only the number of decimal places required for manufacturing precision.
Neatness counts!

## Slide 13: Drawing Appearance – Not Good

## Slide 14: Drawing Appearance – Much Better

## Slide 15: What is a Drawing Template?
A Drawing Template is the foundation for drawing information.
A drawing template specifies:
Sheet (paper) size
Orientation - Landscape or Portrait
Sheet Format
  Borders
  Title block
  Data forms and tables such as bill of materials or revision history

## Slide 16: Drawing Templates Choices in SolidWorks
Standard SolidWorks drawing template
Tutorial drawing template
Custom template
No template

## Slide 17: To Create a New Drawing Using a Document Template:
Click New on the Standard toolbar.
Click the Tutorial tab.
Double- click the drawing icon.
Tutorial Tab
Drawing Icon
Preview

## Slide 18: Sample Drawing Template

## Slide 19: Edit Sheet vs. Edit Sheet Format
There are two modes in the drawing:
Edit Sheet
  This is the mode you use to make detailed drawings
  Used 99+% of the time
  Add or modify views
  Add or modify dimensions
  Add or modify text notes
Edit Sheet Format
  Change the title block size and text headings
  Change the border
  Incorporate a company logo
  Add standard text that appears on every drawing

## Slide 20: Title Block
Contains vital part and/or assembly information.
Each company can have a unique version of a title block.
Typical title block information includes:
Company name | Material & Finish
Part number | Tolerance
Part name | Drawing scale
Drawing number | Sheet size
Revision number | Revision block
Sheet number | Drawn By/Checked By

## Slide 21: To Edit the Title Block:
Right-click in the graphics area, and select Edit Sheet Format from the shortcut menu.

## Slide 22: Editing the Title Block:
Zoom in on the title block.

## Slide 23: Editing the Title Block:
Double-click the note that says <COMPANY NAME>. The PropertyManager and the pop-up formatting toolbar appear.
Enter your school name in the text insertion box.

## Slide 24: Editing the Title Block:
Set the text justification to Align Left and change the size and style of the text font.
Click OK to apply the changes and close the PropertyManager.

## Slide 25: Editing the Title Block:
Position the note so it is centered in the space.

## Slide 26: Customizing the Part Name
Advanced Topic
The name of the part or assembly shown on the drawing changes with every new drawing.
It is not very efficient to have to edit the sheet format and the title block each time you make a new drawing.
It would be nice if the title block would automatically be filled in with the name of the part or assembly that is shown on the drawing.
This can be done.

## Slide 27: Editing the Part Name:
Advanced Topic
Click Note on the Annotation toolbar, or click Insert, Annotations, Note.
The PropertyManager appears.
Click the Link to Property button .

## Slide 28: Editing the Part Name:
Advanced Topic
Click Model in view specified in sheet properties, and choose SW-File Name from the list of properties.
Click OK to add the property.

## Slide 29: Editing the Part Name:
Advanced Topic
In the PropertyManager, set any other text properties such as justification, or font.

## Slide 30: Editing the Part Name:
Advanced Topic
Click OK to apply the changes and close the PropertyManager.

## Slide 31: Advanced Topic
Advanced Topic
Results.
Currently the title block shows the text of the property. However, when the first view is added to the drawing, that text will change to become the file name of the referenced part or assembly.

## Slide 32: Switching to Edit Sheet Mode:
Right-click in the graphics area, and select Edit Sheet from the shortcut menu.
This is the mode you must be in when you make drawings.

## Slide 33: Detailing Options
Dimensioning Standards
Dimensioning standards determine things such as arrowhead style and dimension text position.
The Tutorial drawing template uses the ISO standard.
ISO stands for International Organization for Standardization.
ISO is widely used in European countries.

## Slide 34: Detailing Options
Dimensioning Standards
ANSI is widely used in the United States.
ANSI stands for American National Standards Institute.
Other standards include BSI (British Standards Institution) and DIN (Deutsche Industries-Normen).
Customize the drawing template to use the ANSI standard.

## Slide 35: Detailing Options
Setting the dimensioning standard:
Click Tools, Options.
Click the Document Properties tab
Click Detailing.
Select ANSI from the Dimensioning standard list.
Click OK.

## Slide 36: Detailing Options
Setting text fonts:
Click Tools, Options.
Click the Document Properties tab
Click Annotations Font.
Select the annotation type from the list.

## Slide 37: Detailing Options
Setting text fonts continued:
The Choose Font dialog box opens.
Make the desired changes and click OK.

## Slide 38: Saving a Custom Drawing Template:
Click File, Save As...
From the Save as type: list, click Drawing Templates.
The system automati- cally jumps to the directory where the templates are installed.
Click to create a new folder.

## Slide 39: Saving a Custom Drawing Template:
Name the new folder Custom.
Browse to the Custom folder.
Enter ANSI-MM-SIZEA for the file name.
Click Save.
Drawing templates have the suffix *.drwdot

## Slide 40: Creating a Drawing – General Procedure
Open the part or assembly you wish to detail.
Open a new drawing of the desired size.
Add views: usually three standard views plus any specialized views such as detail, auxiliary, or section views.
Insert the dimensions and arrange the dimensions on the drawing.
Add additional sheets, views and/or notes if required.

## Slide 41: To Create Three Standard Views:
Click Standard 3 View .
Select Tutor1 from the Window menu.
Click OK.
The drawing window reappears with the three views of the selected part.
Drawing View 2
Drawing View 1
Drawing View 3

## Slide 42: Working with Drawing Views
To select a view, click the view boundary. The view boundary is displayed in green.
Drawing views 2 and 3 are aligned with view 1.
Drag Drawing View1 (Front). Drawing View 2 (Top) and Drawing View 3 (Right) move, staying aligned to Drawing View1.
Drawing View 3 can only be dragged left or right.
Drawing View 2 can only be dragged up or down.

## Slide 43: Working with Drawing Views
Hidden line representation.
  Hidden Lines Visible is usually used in orthographic views.
  Hidden Lines Removed is usually used in isometric views.
Tangent edge display.
  Right-click inside the view border.
  Select Tangent Edge, Tangent Edges Removed from the shortcut menu.

## Slide 44: Dimensioning Drawings
The dimensions used to create the part can be imported into the drawing.
Dimensions can be added manually using the Dimension tool .
Associativity
Changing the values of imported dimensions will change the part.
You cannot change the values of manually inserted dimensions.

## Slide 45: To Import Dimensions into the Drawing:
Click Model Items on the Annotation toolbar, or click Insert, Model Items.
Click the Import items into all views check box.
Click the option for Marked for drawing and Eliminate duplicates check box.
Click OK.

## Slide 46: Manipulating Dimensions
Moving dimensions:
  Click the dimension text.
  Drag the dimension to the desired location.
  To move a dimension into a different view, press and hold the Shift key while you drag it.
Deleting dimensions:
  Click the dimension text, and then press the Delete key.
Flipping the arrows:
  Click the dimension text.
  A green dot appears on the dimension arrows.
  Click the dot to flip the arrows in or out.

## Slide 47: Finish the Drawing
Position the views.
Arrange the dimensions by dragging them.
Set hidden line removal and tangent edge display.

## Slide 48: Associativity
Changing a dimension on the drawing changes the model.
  Double-click the dimension text.
  Enter a new value.
  Rebuild.
Open the part. The part reflects the new value.
Open the assembly. The assembly also reflects the new value.

## Slide 49: Multi-sheet Drawings
Drawings can contain more than one sheet.
The first drawing sheet contains Tutor1.
The second drawing sheet contains the Tutor assembly.
Use the B-size landscape (11” x 17”) drawing Sheet Format.
Add 3 standard views.
Add an Isometric view of the assembly. The Isometric view is a model view.

## Slide 50: Three View Drawing of Assembly

## Slide 51: Model Views
A model view shows the part or assembly in a specific orientation.
Examples of model views are:
  Standard Views such as Front, Top or Isometric view.
  User-defined view orientations that were created in the part or assembly.
  The current view in a part or assembly.

## Slide 52: To Insert a model View:
Click model View , or click Insert, Drawing view, Model.
Click inside the border of an existing view.
Important: Do not click directly on one of the parts in the assembly. Doing so will create a named view of that specific part.

## Slide 53: Inserting a Model View:
A selection of model view icons appears in the PropertyManager.
Select the desired view, in this case, Isometric , from the selection.
Place the view in the desired location on the drawing.

## Slide 54: Isometric View Added to Drawing

## Slide 55: Specialized Views
Detail View – used to show enlarged view of something.
Click , or click Insert, Drawing View, Detail.
Sketch a circle in the “source” view.
Position the view on drawing.
Edit the label to change scale.
Import dimensions or drag them into view.

## Slide 56: Specialized Views
Section View – used to show internal aspects of object.
Click , or click Insert Drawing View, Section.
Sketch line in the “source” view.
Position the view on drawing.
Section view is automatically crosshatched.
Double-click section line to reverse arrows.

## Slide 57: eDrawings
Animate, View, and Email eDrawings.
Allows others to view parts, assemblies, and drawings outside of SolidWorks.
Files are compact enough to email.

## Slide 58: Publishing eDrawings
Creating an eDrawing is quick and simple.
Click to publish an eDrawing from any SolidWorks file.
You can create eDrawings from AutoCAD® drawings, too.

## Slide 59: View eDrawings Dynamically
Click Continuous Play to view a continuously running animation of the eDrawing.
Step through the eDrawing animation using Next and Previous .
Click Stop to end the animation.

## Slide 60: Sending eDrawings
Click Send or File, Send to email an eDrawing.
Several email-compatible formats.
The recipient does not need to have the SolidWorks application to view the file.

## Slide 61: Shaded View
By default eDrawing views are shaded.
Click Shaded to view an eDrawing as wireframe.
Click again to view an eDrawing as shaded.

## Slide 62: Resetting the View
Click Home to reset the view to the default.
Home allows you to look at the eDrawing and then quickly return it to the default view.

## Slide 63: 3D Pointer
Helps you to see the orientation of the model in an eDrawing created from a drawing file.
Click to display the 3D pointer.
  Red — X-Axis
  Blue — Y-Axis
  Green — Z-Axis

## Slide 64: Overview Window
Small thumbnail view of the eDrawing.
Click Overview Window to display the Overview window.

## Slide 65: What is PhotoView 360?
A software application that creates realistic images from SolidWorks models.
PhotoView 360 uses rendering effects such as:
Appearances
Lights
Shadows
Backgrounds

## Slide 66: Appearances
Appearances specify the visual properties of a model’s surface.
Properties are:
Color
Mapping
Surface Finish
Illumination

## Slide 67: Image Background
The portion of the graphics area not covered by the model.
Background styles vary in complexity and rendering speed.
Background styles controlled by Scene Editor.
Incorporate advanced rendering effects into a PhotoWorks Scene.
  Shadows
  Reflections

## Slide 68: SolidWorks MotionManager
What is SolidWorks MotionManager?
SolidWorks MotionManager animates and captures motion of SolidWorks parts and assemblies.
SolidWorks MotionManager generates Windows-based animations (*.avi files). The *.avi file uses a Windows-based Media Player.
SolidWorks MotionManager can be combined with PhotoWorks.

## Slide 69: Renderer Options
The Renderer affects the quality of the saved image. There are two options:
SolidWorks screen
PhotoView 360 buffer

## Slide 70: Factors Affecting File Size
Number of frames per second
Renderer used
  PhotoView 360 buffer creates a larger file than SolidWorks screen
If using PhotoView 360 buffer:
  Appearances
  Background
  Shadows
  Multiple-light sources
Video compression
Key frames

## Slide 71: Output
Different forms of output are required for the different phases of the design process
  During Design
  Manufacturing
  Marketing
  Project Support

## Slide 72: Types of Output
Screen prints
Photorealistic prints and image files
Animations
2D Drawings
3D Drawings (eDrawings)
PDF (Portable Document Format)
SolidWorks Files
Non-SolidWorks Files

## Slide 73: Screen Prints
Prints as you would any other document through File, Print menu
  Scaled or full size
  Color will be the same as on the computer screen
  Use Realview if available to make it look more realistic
  Add headers and footers to help identify the print

## Slide 74: Screen Print
RealView Off

## Slide 75: Screen Print
RealView On

## Slide 76: Image Files
From SolidWorks
  JPEG (*.jpg)
  Adobe PhotoShop (*.psd)
  TIFF (*.tif)
  Adobe Illustrator (*.ai)
From PhotoView 360
  Windows Bitmap (*.bmp)
  TARGA (*.tga)
  JPEG (*jpg)
  TIFF (*.tif)
  High Dynamic Range (*.hdr)
  TIFF (*.tif)
  Adobe Illustrator (*.ai)

## Slide 77: Image Files
Raster Images
  Store information about each pixel
  Do not scale well
  Generally larger file sizes
Vector Images
  Store information about where entities start and end
  Scale well
  Generally smaller file sizes

## Slide 78: Image in PowerPoint Slide

## Slide 79: Truck

## Slide 80: The Deck

## Slide 81: Wheel Assembly

## Slide 82: Spring Assembly

## Slide 83: Binding Assembly

## Slide 84: Mountainboard

## Slide 85: Mountainboard

## Slide 86: CODEC
COmpressor/DECompressor
  Used to reduce video file size
  CODEC used to record video file must also be available on machine used to play the video file