## Slide 1
DESIGN PROJECT
Student Guide
BRIDGES

## Slide 2
LEARNING OBJECTIVES
  Understand the different types of truss bridges.
  Learn basic bridge component terminology.
  Design with constraints by applying design intent to the project.
  Explore and understand manufacturing principles.
  Understand the basics of 3D printing.

## Slide 3
BACKGROUND

## Slide 4: FAMOUS BRIDGES - Here’s a list of 10 famous bridges from around the world, along with the purposes they serve:
Golden Gate Bridge (USA)
  Purpose: Connects San Francisco to Marin County, facilitating transportation across the Golden Gate Strait.
  Type: Suspension bridge.
Tower Bridge (UK)
  Purpose: Combines bascule and suspension design to allow pedestrian and vehicle traffic while opening for river traffic on the Thames.
  Type: Bascule and suspension bridge.
Brooklyn Bridge (USA)
  Purpose: Connects Manhattan and Brooklyn, serving as a vital transportation link over the East River.
  Type: Hybrid cable-stayed/suspension bridge.
Sydney Harbour Bridge (Australia)
  Purpose: Connects Sydney’s central business district to its northern suburbs, accommodating vehicles, trains, pedestrians, and cyclists.
  Type: Arch bridge.
Millau Viaduct (France)
  Purpose: Spans the Tarn River valley, reducing traffic congestion in southern France and offering a quicker route.
  Type: Cable-stayed bridge.
Akashi Kaikyō Bridge (Japan)
  Purpose: Links the city of Kobe to Awaji Island, supporting vehicular traffic over the Akashi Strait.
  Type: Suspension bridge.
Rialto Bridge (Italy)
  Purpose: Connects districts across the Grand Canal and is one of Venice’s oldest and most famous pedestrian bridges.
  Type: Stone arch bridge.
Pont du Gard (France)
  Purpose: An ancient Roman aqueduct bridge used to transport water to the Roman colony of Nemausus (modern-day Nîmes).
  Type: Aqueduct bridge.
Zhangjiajie Glass Bridge (China)
  Purpose: A pedestrian bridge offering breathtaking views of the Zhangjiajie Grand Canyon, known for its transparent glass floor.
  Type: Glass-bottom suspension bridge.
Humber Bridge (UK)
  Purpose: Spans the Humber Estuary, connecting Hull and North Lincolnshire, supporting road traffic.
  Type: Suspension bridge.

## Slide 5
TYPES of TRUSS BRIDGES
In Boston, Thomas Pratt and his father Caleb Pratt designed a bridge truss structure that was to become a standard in bridge construction up to World War 2.
It was patented in 1848 by its designers James Warren and Willoughby Theobald Monzani.
A Parker truss bridge is a Pratt truss design with a polygonal upper chord. A "camelback" is a subset of the Parker type, where the upper chord consists of exactly five segments.
The bowstring truss bridge was patented in 1841 by Squire Whipple. A bowstring truss has diagonal load-bearing members.
The Pennsylvania (Petit) truss is a variation on the Pratt Truss. The Pennsylvania truss adds to this design half-length struts or ties in the top, bottom, or both parts of the panels.
A Baltimore truss is similar to a Pratt truss design with additional bracing in the lower section to prevent buckling and add strength. The Baltimore truss style bridge is a simple and very strong design often used for supporting trains.
PRATT
WARREN
PARKER
BOWSTRING
PENNSYLVANIA
BALTIMORE

## Slide 6
BRIDGE TERMINOLOGY
TOP CHORD
BOTTOM CHORD
DIAGONAL
LATERAL BRACE
LATERAL BRACE with SNAPS
ABUTMENT
DECK

## Slide 7
DESIGN TERMINOLOGY
Flat-Pack Design – All or most of the components are flat. During the 3D printing process, this type of design minimizes waste or the need for support material.
Design Intent– In CAD modeling terms, Design Intent is how your model behaves when dimensions are modified. An example of design intent is how you create and dimension a hole in a block. In product design terms, Design Intent is how a product should look, function and feel to the user.
Additive Manufacturing – The construction of a 3D object by adding material layer by layer. 3D printing is an additive manufacturing process.
DFM/DFAM – Design for Manufacturing or Design For Additive Manufacturing. In this activity, it is important to consider the material and capabilities of the 3D printer in order to achieve a functional design with minimal waste.
Nesting – In manufacturing, nesting refers to laying out cutting patterns on raw material to minimizing waste during manufacturing processes, such as laser cutting. In 3D printing, it is the process of laying out parts to fit on the bed of the 3D printer to print several components at one time.

## Slide 8
PROJECT DESIGN INTENT
All components are to be 3D Printed.
Minimize waste using Flat-Pack Design principles.
Snap together assembly, no Fasteners or Adhesives.
The bridge should span at least 350mm.
NOTE: Dimensions are provided for reference only and are not required to meet Design Intent. Units are in millimeters.

## Slide 9
COMPONENT
DESIGN

## Slide 10
Bridge Components
LATERAL BRACE
QTY = 8
LATERAL BRACE WITH SNAPS
QTY = 4
DECKING/PAVEMENT
QTY = 2
DECKING CONNECTOR
QTY = 1
“A” SECTION
QTY = 2
CENTER SECTION
QTY = 3
ABUTMENT
QTY = 2

## Slide 11
COMPONENTS – “A” SECTION
DESIGN INTENT
Incorporates all structural members of a section of the bridge in one part, top and bottom chords, diagonals and verticals.
Has same thickness as the Center Section.
Sits on top of the abutment.
DFAM
Uses Flat-Pack Design, no support material necessary.
Incorporates nesting to print several components at one time.

## Slide 12
COMPONENTS - CENTER SECTION
DESIGN INTENT
Incorporates all structural members of a section of the bridge in one part, top and bottom chords, diagonals and verticals.
Has same thickness as the “A” Section.
DFAM
Uses Flat-Pack Design, no support material necessary.
Incorporates nesting to print several components at one time.

## Slide 13
COMPONENTS – LATERAL BRACE with SNAPS
DESIGN INTENT
Holds 2 bridge sections together at the bottom.
Snaps prevent spreading as force is applied to structure.
Clearance is applied to allow for ease of assembly at the snaps.
DFAM
Designed to minimize support material.
Incorporates nesting to print several components at one time.
Support material is required at overhangs of the snaps.

## Slide 14
COMPONENTS – LATERAL BRACE
DESIGN INTENT
Holds 2 bridge sections together at the top.
Slots are the same thickness as the sections.
DFAM
Designed to minimize support material.
Components are nested to print several at one time.

## Slide 15
COMPONENTS – ABUTMENT
DESIGN INTENT
Supports bridge structure at the ends.
Holds together the bridge sections with the deck.
Base is oriented inwards due to forces applied to the bridge.
DFAM
Designed to minimize support material.
Components are nested to print several at one time.

## Slide 16
COMPONENTS – DECK
DESIGN INTENT
Provides lateral support.
Fits between sides of bridge and abutment.
Designed in context of the assembly.
2 sections joined together with a connector.
DFAM
Designed in 2 sections, due to the requirements of the 3D printer envelope.
Designed to minimize support material.
Components are nested to print several at one time.
CONNECTOR
DECK

## Slide 17
3D PRINTING

## Slide 18
3D PRINTING – Flat-Pack Orientation
Components are Nested.

## Slide 19
3D PRINTING – Standard Orientation
Components are Nested.
Oriented for no support required.

## Slide 20
3D PRINTING – Standard Orientation
Components are Nested
Support required. Use organic support structures to maximize efficiency.

## Slide 21
PROJECT TASKS
Create the following bridge components in CAD:
  Center Section
  “A” Section
  Lateral Brace with Snaps (Bottom)
  Lateral Brace (Top)
  Abutment
  Deck
  Deck Connector
Create an assembly of the bridge in CAD.
Print the physical components on a 3D printer.
Assemble the bridge.

## Slide 22
CLASS DISCUSSION
Question:
Question:
What bridge types have you seen?
How can the design be improved to support more weight or span a greater distance?
Recall the different types of bridges.
Think about the Baltimore Truss bridge design.

## Slide 23
The template slides in the following section are provided for your convenience. We encourage you to customize this presentation for your needs.

## Slide 24
LOREM IPSUM
  XXX

## Slide 25
TIMELINE
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX

## Slide 26
CLASS DISCUSSION
Question:
Question:
Lorem Ipsum
Lorem Ipsum
Lorem Ipsum
Lorem Ipsum