## Slide 1
DESIGN PROJECT
Student Guide
CATAPULT

## Slide 2
LEARNING OBJECTIVES
  Understand different types of catapults.
  Learn basic catapult component terminology.
  Design with constraints by applying design intent to the project.
  Explore and understand manufacturing principles.
  Understand the basics of 3D printing.

## Slide 3
BACKGROUND

## Slide 4
BACKGROUND
The inspiration for this design is the Roman Onager, a siege weapon used to knock down the walls of a fortress, employed by the armies of ancient Rome. Due to the nature of its design, it was named onager, because, when operated, it kicked like a mule! An onager is a species of wild African ass which was characterized as an exceptionally fast runner with an unruly disposition.

## Slide 5
CATAPULT TERMINOLOGY
FACE PLATE
SIDE PLATE
SIDE PLATE
BACK SUPPORT
FRONT SUPPORT
BASKET ARM
FOAM BALL
#2 RUBBER BAND

## Slide 6
DESIGN TERMINOLOGY
Flat-Pack Design – All or most of the components are flat. During the 3D printing process, this type of design minimizes waste or the need for support material.
Design Intent– In CAD modeling terms, Design Intent is how your model behaves when dimensions are modified. An example of design intent is how you create and dimension a hole in a block. In product design terms, Design Intent is how a product should look, function and feel to the user.
Additive Manufacturing – The construction of a 3D object by adding material layer by layer. 3D printing is an additive manufacturing process.
DFM/DFAM – Design for Manufacturing or Design For Additive Manufacturing. In this activity, it is important to consider the material and capabilities of the 3D printer in order to achieve a functional design with minimal waste.
Nesting – In manufacturing, nesting refers to laying out cutting patterns on raw material to minimizing waste during manufacturing processes, such as laser cutting. In 3D printing, it is the process of laying out parts to fit on the bed of the 3D printer to print several components at one time.

## Slide 7
PROJECT DESIGN INTENT
  3D Printed
  Flat-Pack Design
  Launches 7/8” Diameter Foam Ball
  Rubber Band Powered
  No Fasteners or Adhesives
Face Plate sits on a groove in the Front Support.
Basket Arm rotates about the centerline of the assembly.
Basket Arm strikes the Face Plate at the SAME angle.
Ribs are used to reinforce the strike plate and the Basket Arm.
Hooks on the Basket Arm and the Side Plates hold the rubber band in place.

## Slide 8
COMPONENT
DESIGN

## Slide 9
COMPONENTS – SIDE PLATE
DESIGN INTENT
Side plates are identical.
Slots connect the side plates to the Front and Back Supports, and the Face Plate.
Pivot hole for Basket Arm is centered on part.
DFAM
Uses Flat-Pack Design, no support material necessary.
Components can be nested to print several at one time.
NOTE: Dimensions are provided for reference only and are not required to meet Design Intent. Units are in inches.

## Slide 10
COMPONENTS – FRONT SUPPORT
DESIGN INTENT
Same thickness as Back Support.
Slots connect to Side Plates.
Groove on back side for Face Plate to rest on.
DFAM
Uses Flat-Pack Design, no support material necessary.
Components can be nested to print several at one time.
Groove for Face Plate

## Slide 11
COMPONENTS – BACK SUPPORT
DESIGN INTENT
Same thickness as Front Support.
Slots connect to Side Plates.
Notch allows Basket Arm to rotate fully.
DFAM
Uses Flat-Pack Design, no support material necessary.
Components can be nested to print several at one time.
Notch

## Slide 12
COMPONENTS – FACE PLATE
DESIGN INTENT
Notches slide into slots in Side Plates.
The Basket Arm strikes the Face Plate at a reinforced feature that has an angle to increase trajectory.
The front of the Face Plate rest on a ledge in the back of the Front Support.
The design of the Face Plate can be personalized.
DFAM
No support material necessary.
Components can be nested to print several at one time.
Notches
Fits in the groove on the Front Support
Basket Arm strikes here

## Slide 13
COMPONENTS – BASKET ARM
DESIGN INTENT
Basket is designed to hold a 7/8” diameter foam ball.
Rotates freely in corresponding holes of Side Plates.
Has a hook on backside to hold a rubber band in place.
Design in the context of the assembly.
DFAM
Orient the part so basket is facing up.
Use organic supports, if possible to, reduce support.
Hook
Rotation Pin

## Slide 14
3D PRINTING

## Slide 15
3D PRINTING – Flat-Pack Orientation
  Components are Nested.

## Slide 16
3D PRINTING – Standard Orientation
Support required. Use organic support structures to maximize efficiency.

## Slide 17
PROJECT TASKS
Create the following catapult components in CAD:
  Side Plate
  Front Support
  Back Support
  Faceplate
  Basket Arm
Create an assembly of the catapult in CAD.
Print the physical components on a 3D printer.
Assemble the catapult.

## Slide 18
CLASS DISCUSSION
Question:
Question:
  How will the trajectory of the ball be affected by changing the angle or size of the area where the Basket Arm strikes the Face Plate?
  How will different types of elastic bands affect the power of the machine?
Consider the surface where the basket arm strikes the Face Plate.
Think of how the catapult is powered.

## Slide 19
The template slides in the following section are provided for your convenience. We encourage you to customize this presentation for your needs.

## Slide 20
LOREM IPSUM
  XXX

## Slide 21
TIMELINE
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX

## Slide 22
CLASS DISCUSSION
Question:
Question:
Lorem Ipsum
Lorem Ipsum
Lorem Ipsum
Lorem Ipsum