## Slide 1
DESIGN PROJECT
Student Guide
NAME TAG

## Slide 2
LEARNING OBJECTIVES
  Learn basic CAD design terminology
  Explore and understand DFAM principles
  Understand the basics of 3DPrinting

## Slide 3
BACKGROUND

## Slide 4
PART DETAILS
BODY
FILLETS
LOOP
TEXT

## Slide 5
DESIGN TERMINOLOGY
Flat-Pack Design – All or most of the components are flat. During the 3D printing process, this type of design minimizes waste or the need for support material.
Design Intent– In CAD modeling terms, Design Intent is how your model behaves when dimensions are modified. An example of design intent is how you create and dimension a hole in a block. In product design terms, Design Intent is how a product should look, function and feel to the user.
Additive Manufacturing – The construction of a 3D object by adding material layer by layer. 3D printing is an additive manufacturing process.
DFM/DFAM – Design for Manufacturing or Design For Additive Manufacturing. In this activity, it is important to consider the material and capabilities of the 3D printer in order to achieve a functional design with minimal waste.
Nesting – In manufacturing, nesting refers to laying out cutting patterns on raw material to minimizing waste during manufacturing processes, such as laser cutting. In 3D printing, it is the process of laying out parts to fit on the bed of the 3D printer to print several components at one time.

## Slide 6
PROJECT DESIGN INTENT
All components are to be 3D Printed.
Minimize waste using Flat-Pack Design principles.

## Slide 7
COMPONENT
DESIGN

## Slide 8
COMPONENT- NAME TAG
DESIGN INTENT
Fillets are added at corners to remove sharp edges and strengthen the design.
Text is extruded as an emboss, up to the same level as the upper edge.
DFAM
Uses Flat-Pack Design (no support material necessary.
Components are nested to print several at one time.

## Slide 9
3D PRINTING

## Slide 10
3D PRINTING – Standard Orientation
Oriented for no support required.

## Slide 11
3D PRINTING – Flat-Pack Orientation
Components are Nested.

## Slide 12
PROJECT TASKS
Create the Name Tag component in CAD.
Print the physical components on a 3D printer.
Tie the Name Tag to a bag or backpack with a twine or string, or add a split key ring and keys.

## Slide 13
CLASS DISCUSSION
Question:
Question:
What are the implications of changes to the length, width, and thickness of the model?
How can the personalized text be engraved rather than embossed?
Consider changes to the size of the model.
Think about the extruded text.

## Slide 14
The template slides in the following section are provided for your convenience. We encourage you to customize this presentation for your needs.

## Slide 15
LOREM IPSUM
  XXX

## Slide 16
TIMELINE
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX

## Slide 17
CLASS DISCUSSION
Question:
Question:
Lorem Ipsum
Lorem Ipsum
Lorem Ipsum
Lorem Ipsum