## Slide 1
DESIGN PROJECT
Student Guide
TENSEGRITY
TABLE

## Slide 2
LEARNING OBJECTIVES
  Design, model, and assemble a tensegrity table capable of supporting a small object.
  Learn physics concepts, such as tension, gravity, and mechanical design principles, including tolerance and CAD modeling techniques.
  Understand how the balance of tension and compression creates a stable structure.

## Slide 3
BACKGROUND

## Slide 4
BACKGROUND
Tensegrity structures can be found in both natural and human-made objects, such as bridges, stadium roofs, tents, and even in the human body. The tensegrity concept relies on balancing structural components to ensure integrity.
Here are a few examples of Tensegrity structures found around the world:
NASA Super Ball Bot (USA)
Skylon Tower (Britain)
Denver International Airport (USA)
Science World Vancouver (Canada)
Needle Tower (USA)
Munich Olympic Stadium (Germany)
Montreal Biosphere (Canada)
Kurilpa Bridge(Australia)

## Slide 5
TENSEGRITY TABLE IDEAS

## Slide 6
DESIGN TERMINOLOGY
Flat-Pack Design – All or most of the components are flat. During the 3D printing process, this type of design minimizes waste or the need for support material.
Design Intent– In CAD modeling terms, Design Intent is how your model behaves when dimensions are modified. An example of design intent is how you create and dimension a hole in a block. In product design terms, Design Intent is how a product should look, function and feel to the user.
Additive Manufacturing – The construction of a 3D object by adding material layer by layer. 3D printing is an additive manufacturing process.
DFM/DFAM – Design for Manufacturing or Design For Additive Manufacturing. In this activity, it is important to consider the material and capabilities of the 3D printer in order to achieve a functional design with minimal waste.
Nesting – In manufacturing, nesting refers to laying out cutting patterns on raw material to minimizing waste during manufacturing processes, such as laser cutting. In 3D printing, it is the process of laying out parts to fit on the bed of the 3D printer to print several components at one time.

## Slide 7
COMPONENT
DESIGN

## Slide 8
OVERALL DESIGN INTENT
All components must be 3D printed.
Minimize waste using flat-pack design principles.
The assembly is a press-fit design, requiring no glue or adhesives.
The table must support a small object.

## Slide 9
COMPONENTS – BASE
DESIGN INTENT
Hooks are used for attaching the two subassemblies together with fishing line or other suitable alternative.
The T Cutout is designed using the assembled parts as a reference.
DFAM
3D Printed upside down to eliminate support material.

## Slide 10
COMPONENTS – ARM
DESIGN INTENT
The T slot drives the cutout in the Base.
Overall size is to be smaller than the Base.
DFAM
3D Printed on the side to minimize support material.

## Slide 11
3D PRINTING

## Slide 12
3D PRINTING
Components are Nested*
  *Actual nesting arrangement depends on printer used. Creality K2 Plus printer shown.

## Slide 13
PROJECT TASKS
Create the following components in CAD:
  Base
  Arm
Create an assembly of the Base and Arm in CAD.
Create a cutout in the Base to mount the Arm.
Print the physical components on a 3D printer.
Assemble the table.
Balance an object.

## Slide 14
CLASS DISCUSSION
Question:
Question:
What are the underlying physics of the structure?
What other examples of Tensegrity can you identify?
Why did some tables collapse while others remained stable?
How do minor adjustments in string tension affect stability?
Think about the concept of Tensegrity.
Think about the assembled table.

## Slide 15
The template slides in the following section are provided for your convenience. We encourage you to customize this presentation for your needs.

## Slide 16
LOREM IPSUM
  XXX

## Slide 17
CLASS DISCUSSION
Question:
Question:
Lorem Ipsum
Lorem Ipsum
Lorem Ipsum
Lorem Ipsum

## Slide 18
TIMELINE
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX