## Slide 1
DESIGN PROJECT
Student Guide
WIND-POWERED SAW

## Slide 2
LEARNING OBJECTIVES
  Convert between different types of mechanical energy.
  Understand the basics of torque, friction, and rotational dynamics.
  Use CAD to explore different possibilities before manufacturing.
  Design with constraints – apply Design Intent to a project.
  Understand the basics of 3D Printing (fits, tolerances, and limitations).
  Purchase components and design around existing parts.

## Slide 3
BACKGROUND

## Slide 4
HISTORY
Ancient Persia
Medieval Europe
Pre-Industrial Revolution

## Slide 5
DESIGN TERMINOLOGY
Design Intent – In CAD modeling terms, Design Intent is how your model behaves when dimensions are modified. In product design terms, Design Intent is how a product should look, function and feel to the user.
Additive Manufacturing – The construction of a 3D object by adding material layer by layer. 3D printing is an additive manufacturing process.
Power Transmission – The process of transferring energy from one form to another. In the case of this project, rotational energy into sawing motion.
Gear Ratio – The relationship between gear sizes that affects speed and torque.
Aerodynamics – How airflow interacts with blade design to maximize wind capture.

## Slide 6
COMPONENT
DESIGN

## Slide 7
Fan
Base
Support (2x)
Bearing (2x)
Dowel (2x)
Crank (Cam)
Saw Blade
Dowel Holder
COMPONENTS
(not to scale)
Screw

## Slide 8
COMPONENTS - PURCHASED
  Much of the design will depend on the dimensions of the purchased components.
  Included example files are for a 6”diameter fan blade and 5/16” dowel.
  All other measurements in MM.
Steel Pan Head Phillips Screw, M3 x 0.5 mm Thread, 6 mm Long

## Slide 9
Wall Dovetails
Dowel Holder Dovetail
All dimensions in MM
COMPONENTS - BASE
DESIGN INTENT
Must securely hold supports and dowel holder.
Must be large enough to space components apart, yet small enough to fit on the 3D Printer bed.
Conserve material where appropriate.
DFAM
Research your 3D Printer settings to determine an angle that is printable without using supports.

## Slide 10
COMPONENTS - WALL
All dimensions in MM
Wall Dovetail
DESIGN INTENT
Must securely hold the bearing.
Must securely interface with the Base.
Conserve material where appropriate.
DFAM
Research your 3D Printer settings to determine a dovetail angle that is printable without using supports.
Create test prints to verify fits before printing the final component.

## Slide 11
COMPONENTS - CAM
All dimensions in MM
DESIGN INTENT
Must convert rotational motion into linear motion.
Optimize torque and speed.
Must fit tightly on the shaft.
DFAM
Research your 3D Printer settings to determine how much to oversize or undersize holes to get the intended fit.

## Slide 12
COMPONENTS – DOWEL HOLDER
All dimensions in MM
Dowel Holder Dovetail
DESIGN INTENT
Must securely interface with the Base component.
Must hold the dowel as it is being cut.
Must not interfere with the saw blade.
DFAM
Research your 3D Printer settings to determine a dovetail angle that is printable without using supports.
Create test prints to verify fits before printing the final component.

## Slide 13
3D PRINTING

## Slide 14
3D PRINTING - NESTING
  Arrange as many components as possible on the build plate.

## Slide 15
3D PRINTING – SUPPORT MATERIAL
  Minimize support material where possible.
Less support material - easier to remove.
More support material - difficult to remove.

## Slide 16
PROJECT TASKS
Research and purchase components.
Model the following components in CAD:
  Base
  Walls
  Cam
  Dowel Holder
3D Print small sections to test fits for the following:
  Wall dovetail
  Bearing hole
  Cam holes
  Dowel Holder dovetail
3D Print full assembly
Assemble all the components
Cut a dowel

## Slide 17
CLASS DISCUSSION
Question:
Question:
What other methods could be used to make the custom components?
How could this design be modified to be more efficient or use a different power source?
Explore Manufacturing Methods
Explore Alternative Designs

## Slide 18
The template slides in the following section are provided for your convenience. We encourage you to customize this presentation for your needs.

## Slide 19
LOREM IPSUM
  XXX

## Slide 20
TIMELINE
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX
XXX

## Slide 21
CLASS DISCUSSION
Question:
Question:
Lorem Ipsum
Lorem Ipsum
Lorem Ipsum
Lorem Ipsum