## Slide 1: Bridge Design Project
Using SolidWorks and SolidWorks Simulation to design, test and build structures

## Slide 2: Introduction- Prerequisites
SolidWorks files come in three basic types; parts, assemblies and drawing
Complete the following tutorials that are integrated in the SolidWorks software:
  Lesson 1 - Parts
  Lesson 2 - Assemblies
  Lesson 3 – Drawings

## Slide 3: 1 - Structure Design

## Slide 4: What are Trusses?
Trusses are simple structures used as bridges for railroads, auto and foot traffic; capable of carrying large loads across spans. They consist of a road or rail surface, 2 walls and sometimes bracing between the walls.

## Slide 5: Longer Spans
For longer spans, the truss structure can be repeated several times.

## Slide 6: Truss Types
The Warren truss, shown at right, is one of the simplest and most economical types. It can even be used upside down, in this case with added vertical members.

## Slide 7: Truss Types (continued)
The Pratt (above) and Howe (below) are other common types. We will look at a truss similar to the Pratt truss.

## Slide 8: Truss Walls
The side walls of the truss are much more than walls that keep the trains or cars from falling off the truss. They are used to absorb and direct the loads placed on the truss such as trains cars.

## Slide 9: Beams
Trusses are made up of beams that are held together by bolts, welds or rivets. A common example of a beam is a closet rod used to hang clothes.
Beams have the same cross section.

## Slide 10: External Loads
External Loads are forces that are applied to the beam. A common load on a beam would be weight, such as a train car. Loads are usually applied over an area of the beam.

## Slide 11: Bending and Deflection
Bending is caused by a load that is applied to a beam. The load causes the beam to bend and move in the direction of the load. The deflection is how far the beam moves from it’s original position. The larger the load, the larger the deflection. The “worst case” deflection occurs when the load is at the center of the beam.

## Slide 12: Tension and Compression
While the beam is bending, things are happening within the beam. The top portion of the beam (the face the load is applied) compresses (pushing ends together) while the opposite face sees tension (pulling ends apart).

## Slide 13: Stress
Stress measures what happens inside the beam when forces are applied. It is defined as force divided by area, common units being Pascals (Pa), Megapascals (Mpa) or pounds per square inch (psi).
Stress can cause the beam to break under high loads. Analysis provides maps that show areas of high and low stress.

## Slide 14: Yield Strength
How much can the beam take before it breaks? We use the Yield Strength as the limit of the beam’s strength based on stress.
Actually it measures the point where a beam bends and remains in the bent shape.
Both the material and beam section contribute to the strength.

## Slide 15: Strength of Beams
Strength
Cross Section
Shape
Material
The cross sectional shape influences the strength.
Using a stronger material (steel rather than wood) makes the beam stronger.

## Slide 16: Cross Section Shape
Stacking two or three beams as shown in the image makes the beam harder to bend and stronger against a load.

## Slide 17: Section Depth
The deeper the section (left) the stronger the material. Wider sections (right) help a little but not that much.
The reason that deeper beams are stronger is the area moment of inertia. This is calculated using the width (b) and height (h) dimensions of the section.

## Slide 18: Area Moment of Inertia
For a square section that measures 3.175 mm (0.3175 cm or 1/8”) on a side, the area moment of inertia is:
1 section = 8.47 base
2 stacked = 67.75 8X stronger
2 side by side = 16.94 2X stronger
3 stacked = 228.64 27X stronger

## Slide 19: Materials
The material used to create the beam has a great impact on it’s strength. Although there are many varieties of wood and alloys of metals, generally metal is stronger then wood.
Note that wood, unlike metals, has a grain that makes it’s strength different in different directions.

## Slide 20: Steel Beams
The deeper beam starts to look like the steel beams used in construction of trusses, and buildings, channels, I-beams and tubes.

## Slide 21: Cross Bracing
Cross bracing stiffens the structure by preventing rotation at the joints.
Using drinking straws pinned at the ends shows the difference that a brace can make.

## Slide 22: 2 – Using the Beam Calculator

## Slide 23: Beam Calculator
The Beam Calculator can be used to get an estimate of the displacement. This can be used to make sure that the analysis is within expectations.

## Slide 24: 3 – Analyzing the Structure

## Slide 25: Analysis Stages
Model
Pre-Processing
Analysis
Post-Processing
A Structural Analysis has several stages that are followed in order.
  In SolidWorks:
    Model is where the geometry is created.
  Using SolidWorks Simulation:
    Pre-Processing is used to add materials, fixtures and loads.
    Analysis is where the input is “run” through the analyzer.
    Post-Processing allows you to see the results.

## Slide 26: Design Cycle
The Design Cycle is used to “iterate” changes by returning to the original design to change the model. The changes alter the results of the analysis.
SolidWorks
SolidWorks Simulation
Satisfied?
Prototype
No
Yes
Design
Cycle

## Slide 27: Fixtures and External Loads
Fixtures prevent movement of portions of the structure.
External Loads apply forces to the structure.

## Slide 28: Material
The material selected supplies data to the analysis in the form of numeric properties.

## Slide 29: Joints
Joints are automatically created at the intersections of the beam centerlines.

## Slide 30: Fixtures
The fixtures are applied by selecting joints in the model.

## Slide 31: Loads
The External Loads are applied by selecting joints in the model.

## Slide 32: Mesh and Run
Meshing creates beam elements and nodes that represent the model shape.

## Slide 33: 4 - Making Design Changes

## Slide 34: Changes
Using different models, follow the changes in the model and the changes in capacity of the structure.

## Slide 35: 5 – Using an Assembly

## Slide 36: Collision Detection
In an assembly, components can be checked for collision, interference or clash.

## Slide 37: Changing Dimensions
The dimensions that define the shape of the model can also be used to change the size of the model.

## Slide 38: 6 – Making Drawings of the Structure

## Slide 39: Drawings
The drawing includes a view of the model, a cut list and balloons.

## Slide 40: 7 – Reports and eDrawings

## Slide 41: eDrawings
HTML (web format) reports can be generated from the post-processor data.
An eDrawing can be used to send information to other users.

## Slide 42: 8 – Building and Testing the Structure

## Slide 43: Construction Aids
The PDF files Measuring Chart and Construction Guide can be used to make construction easier.

## Slide 44: Building the Structure
Distribute 1/8" x 1/8" x 24" balsa sticks, glue and cutters.
Cut, glue and assemble structure per instructions.

## Slide 45: Testing the Structure (setup)
Set up sawhorses or tables to represent the 350 mm span.
Place the bridge and load plate across the sawhorses or tables.
Make sure to wear eye protection!

## Slide 46: Testing the Structure (test weight)
Use a drawstring bag or bucket with wire attached.
Pass drawstring or wire through hole in load plate and pin in place.
Load bag or bucket with weighted objects until breakage occurs.

## Slide 47: 9 – Weldment Profiles and Structural Members

## Slide 48: Weldment Profiles
2D sketches saved as library features.
Must be placed in folder under the main weldment profiles folder.
The default weldment profiles are structural steel shapes.
General purpose weldment profiles should have an endpoint or point at any possible placement option (see the default types).

## Slide 49: Structural Members
2D or 3D sketches defining the position and size of the weldment profiles.
Trimming between structural members is done by using Groups or with additional work after creating the weldment.
Multiple weldment profile types can be used to define structural members in the same weldment.